## Slide 1
0xAA Command

## Slide 2
Operating Steps
①
File Starting Location
②
File to VP
③
VP to Flash

## Slide 3
16MB Flash
1. File Starting Location

## Slide 4
256KB storage block
13, 14, 22,32 files are stored in 256KB
Mode 1
64 pcs

## Slide 5
32KB
data block
0xAA command is based on 32KB data block
Mode 2
512 pcs

## Slide 6
File Starting Location
13.bin=13*256/32=104=0x0068
14.bin=14*256/32=112=0x0070
22.bin=22*256/32=176=0x00B0
32.icl=32*256/32=256=0x0100
Based on 32KB data block

## Slide 7
2. File to VP
5AA5 F3 82 8000 14 44 47 55 53 5F 04 00 00...
5AA5 F3 82 8078 00 00 ...
VP+0x78
Next command:
0xF3=
243
Command
length
Frame header
Write
command
VP
address
240 bytes data/command
1*VP address=2 bytes
240 bytes/2=120=0x78(VP address)

## Slide 8
240 bytes data
Use Uedit32 to open the file

## Slide 9
240 bytes data
16 bytes*15 =240bytes

## Slide 10
3. VP to Flash
5AA5 0F 82 00AA 5A 02 0100 8000 00*6
0x0F=15
Command
length
Frame header
Write
command
System VP
address
D11
Enable
flag
D9:D8
file
starting location
D10
Operation mode
D7:D6
VP
address
D5:D0
Undefine,write 00
15 bytes
Reset command:
5AA5 07 82 0004 55AA 5AA5

## Slide 11
Project File
32.icl
21:00pm
Project 1
14:00pm
Project 2
13.bin
14.bin
22.bin